## Slide 1: FAA Building Blocks Leading to UAS Integration Emerging Trends

## Slide 2: UAS Traffic Management (UTM) Concept
An airspace management solution to enable multiple UAS operations conducted beyond visual line-of-sight where air traffic services are not provided.

## Slide 3: What is UTM?
UTM is an “traffic management” ecosystem for uncontrolled operations
UTM is separate, but complementary system to the Air Traffic Management (ATM) system
UTM utilizes industry’s ability to supply services under FAA’s regulatory authority where these services do not exist
UTM development will ultimately identify services, roles/responsibilities, information architecture, data exchange protocols, software functions, infrastructure, and performance requirements for enabling the management of low-altitude uncontrolled UAS operations
How to enable multiple BVLOS operations in low-altitude airspace?
UTM addresses critical gaps associated with lack of support for uncontrolled operations

## Slide 4: UTM Principles & Services for Safe Integration
Principles
Users operate in airspace volumes as specified in authorizations
Authorizations are issued based on type of operation & operator/vehicle performance
UAS stay clear of each other
UAS and manned aircraft stay clear of each other
UAS operator has complete awareness of airspace and other constraints
Public safety UAS have priority over other UAS
Key UAS-related services
Authentication
Airspace configuration and static and dynamic geo-fence definitions
Weather and wind prediction and sensing
Conflict avoidance (e.g., airspace notification)
Demand/capacity management
Large-scale contingency management (e.g., GPS or cell outage)

## Slide 5: Value of UTM
√ Higher density UAS operations
√ Beyond visual light of sight (BVLOS) UAS operations
√ Manned and unmanned vehicle operations coordination
√ Unmanned vehicle operations coordination through agreed upon data/information exchanges about each others’ operations and with FAA NAS systems
√ Exceptions handling
√ Beyond Part 107 operations– e.g, entry into controlled airspace

## Slide 6: UTM Architecture

## Slide 7: Enabling Future Opportunities
UAS could safely prototype technology that will revolutionize flight
  Automation & Flight Controls
Passenger carrying, highly-automated aircraft
  Private Funding vs. Govt. R&D
Planning Workshop for Automation Strategy – Planned Steps to Future
  Collaboration FAA, NASA, industry, academia, municipalities
Notes: Can companies vs. governments be enablers?

## Slide 8: Future Technology Opportunities
UAS will safely prototype technology that will revolutionize flight
  Automation & Flight Control Technology
  Auto Collision Avoidance - Air/Ground
  Automatic Landing Systems
  Refuse to Crash Logic
  Propulsion Systems
Passenger carrying, highly automated aircraft

## Slide 9: Many EVTOL Concepts
https://youtu.be/BSFVvhQP7ws https://youtu.be/ohig71bwRUE

## Slide 10: Uber – Future Transportation
Need To Build Steps Towards Future
Partnerships - Industry, FAA, NASA, Academia, Municipalities
Key is How Automation Can Perform Pilot Functions Safely

## Slide 11: Ehang From China

## Slide 12: Airbus From Europe

## Slide 13: Joby – from USA

## Slide 14: Evolo - Germany